## Slide 1: CSCI 1103 CS 1 Honors
Meeting 26: Friday 10/30
Applications: Working with Digital Audio

## Slide 2: Today
Sound Waves
Analog Recording
Pulse Code Modulation and Digital Recording
Uncompressed Sound Protocols:
  CDs, Wave Files
  Working with Wave Files
Sound Protocols with Compression:
  MP3s

## Slide 3: Humans “hear” Fluctuations in Air Pressure

## Slide 4: Waves
length of a complete wave (cycle)
measured in meters (m)
amplitude

## Slide 5: Frequency
Cycles per second
Measured in Hertz (Hz, hz)

## Slide 6
Amplitude = Loudness
Frequency = Pitch

## Slide 7
Human Hearing: 20Hz – 20KHz; Speech: 340Hz – 3KHz

## Slide 8: Waves are Additive
Chart: 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1


## Slide 9: Asynchronous Waves
Chart: 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1



 | 1 | 2 | 3 | 3 | 2 | 1 | 1 | 2 | 3 | 3 | 2 | 1 | 1 | 2 | 3 | 3 | 2 | 1 | 1 | 2 | 3 | 3 | 2 | 1 | 1 | 2 | 3 | 3 | 2 | 1 | 1 | 2 | 3 | 3 | 2 | 1

## Slide 10: Waves are Additive
Chart: 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1



 | 1 | 2 | 3 | 3 | 2 | 1 | 1 | 2 | 3 | 3 | 2 | 1 | 1 | 2 | 3 | 3 | 2 | 1 | 1 | 2 | 3 | 3 | 2 | 1 | 1 | 2 | 3 | 3 | 2 | 1 | 1 | 2 | 3 | 3 | 2 | 1
 | 2 | 4 | 6 | 7 | 7 | 7 | 8 | 10 | 11 | 10 | 8 | 6 | 5 | 5 | 5 | 4 | 3 | 3 | 4 | 6 | 8 | 9 | 9 | 9 | 9 | 9 | 9 | 8 | 6 | 4 | 3 | 3 | 3 | 3 | 2 | 1
Audio signal

## Slide 11: Recording Audio
Audio signal sensed by a transducer and recorded on a physical artifact, i.e., a record
Record has a co-designed “player” that uses the recording to reconstruct the recorded signal and to amplify it so that it can drive a “speaker” which emits the acoustic signal

## Slide 12: Transducers
A transducer is a device that converts one type of energy to another or to a physical attribute.
Examples: Ears, Microphones, Speakers, Voice Boxes, Radios, Televisions, Sonar Devices, ….

## Slide 13: Transducers : microphones e.g.

## Slide 14: Pulse Code Modulation
Break time up into discrete intervals;
Record the integer quantifying the amplitude at each interval;
The audio signal is represented by the sequence of discrete samples.

## Slide 15: Digital Audio and PCM

## Slide 16: Digital Audio
Bit Depth : How many bits are used to record a given amplitude. We’ll use 16-bit samples.
Sample Rate : How many samples are required for one second? CDs use 44.1K samples/sec. We’ll use 11,025 samples/sec.

## Slide 21
Middle C
A4
A3

## Slide 22
Middle C
A4
220 Hz
440 Hz
A3

## Slide 23: Well-tempered Scale
What frequency is associated with a give note?
Given a frequency f0 of some fixed note, (typically A4 = 440Hz):
fn = f0 * 2n/12
where n is the number of half-steps from f0.

## Slide 26: Nyquist/Shannon Sampling Theorem
If a signal contains no frequencies higher than W cycles per second, it is completely determined by giving its ordinates at a series of points spaced 1/(2W) seconds apart.

## Slide 27: Psychoacoustic Factors
Since most humans top-out at 22KHz, recordings that sample at 44KHz should capture everything that humans can hear.
Most experts believe that humans can only resolve between 16 and 18 bits per sample.

## Slide 28: Digital Audio
Various representation protocols, some proprietary, some public
representation protocols and format information packed into “headers”
software parses the header to “understand” the layout of the data

## Slide 29: Digital Audio
Bit-stream may or may not:
  be packaged-up with error detection/correction information
  be compressed
  be encrypted (e.g., Digital Rights Management DRM). More on these topics later

## Slide 30: Uncompressed Digital Audio
Sony Compact Discs
Microsoft WAV Files

## Slide 31: WAV Protocol
Microsoft WAV protocol : uncompressed PCM
3 Chunks:

## Slide 32: WAV Format Chunk

## Slide 33: WAV Data Chunk

## Slide 34: Compressed Digital Audio
Many different protocols: MP3, OGG, ACC, M4p, …
MP3: a de facto standard, reasonable fidelity + small size
Motion Picture Experts Group (MPEG)
  1991: MPEG-1 Standard, Audio Layer 3, aka MP3 (not to be confused with MPEG-3).
User specifies desired bits/sec for audio. E.g., at 128 bps, 11 X compression .vs. CD file.
Uses both lossy and lossless compression

## Slide 35: Compression
Lossless Compression: the data can be compressed and then expanded without loss of information (more on this later)
Lossy Compression: when we compress the data we’ll lose information (but it won’t matter)